## Slide 1
IRI Mobile Measuring
CEE508: Pavement Rehabilitation and Maintenance
GROUP 5
Watheq, Sina, Juan Pablo

## Slide 2: Introduction
Conclusion
Evaluation
Data Analysis
Roadway network is a very important asset
  Good management of this asset is crucial
Pavement roughness measurement is necessary
  An acceptable reflection of overall pavement condition
  However, can be costly; especially when frequent
Different low-cost alternatives are available
  Including mobile phone apps
RoadLab Pro software
Introduction

## Slide 3: RoadLab Pro
Conclusion
Evaluation
Data Analysis
A mobile phone app that reports IRI at roughly 100-m intervals
  Developed by SoftTeco; funded by a World Bank project in 2018
  Available for both Android and iOS
  Uses kinematics to estimate IRI
    Converts accelerometer data into IRI measurements
    Phone should be mounted as vertically as possible
    Uses GPS for location
  Intended to obtain road conditions in developing countries
Introduction

## Slide 4: Software Overview
Conclusion
Evaluation
Data Analysis
Driving with at least 15km/hr
Gives the option of choosing car's suspension
  Hard
  Soft
  SUV
  Custom
Takes almost continuous measurements
  Reports results every 100m
  Available in SI units
Open source app (free)
Can be linked to online drives (e.g. Dropbox)
Introduction
RoadLab Pro Manual

## Slide 5: Research Motivation
Conclusion
Evaluation
Data Analysis
Cost
  Every municipal entity has a fleet of moving cars (almost no additional cost!)
  Compared to around $120/mile for Data Collection
    Vans (DCV)
Practicality
  Simplicity compared to profilographs, etc.
Accuracy??
  Can it be accurate enough for some applications?
Introduction
Sina Anesteh

## Slide 6: Research Objectives
Objective A: Assess the accuracy, capabilities of handheld measuring of IRI values
Conclusion
Evaluation
Data Analysis
Introduction
Objective B: Investigate possible applications of the software based on the its respective performance through machine learning
Notes: So once we have this software for which we overall understand how it works, we want to test it. Of course, we want to measure how it performs with “Real measurements”, so we go and speak with the people at Champaign public Works. We get their professionaly measured IRI data, taken by Aptech during the summer.
But before even comparing that, do we even know if the results of the app itself are consistent? We know that there are mechanical factors that could impact accelerometer. We know there are multiple settings that could influence the measurements. How do we go about this?

## Slide 7: Accuracy analysis
Step 1: Compare measurements varying internal parameters.
  How repeatable are the measurements?
Step 2: Compare with existing measurements
  Given IRI data for the city of Champaign, how do we compare?
Conclusion
Evaluation
Data Analysis
Introduction
Notes: So once we have this software for which we overall understand how it works, we want to test it. Of course, we want to measure how it performs with “Real measurements”, so we go and speak with the people at Champaign public Works. We get their professionaly measured IRI data, taken by Aptech during the summer.
But before even comparing that, do we even know if the results of the app itself are consistent? We know that there are mechanical factors that could impact accelerometer. We know there are multiple settings that could influence the measurements. How do we go about testing this?
We compare within our measurmenets and with champaigns.

## Slide 8: 1) Variation of Internal Parameters
SUV – Sedan Speed Surface Type
Conclusion
Evaluation
Data Analysis
Introduction
Notes: Given our limited time, we draw a scope. We will vary the following variables and analyse the impact.
Chose Car type: Due to different suspension
Choose speed: possible different impact on wavelengths captured
Surface type: Possible difference due to construction, or state of the road

## Slide 9: Car Type
SUV A.K.A Blue Sapphire
Sedan A.K.A Black Diamond
Conclusion
Evaluation
Data Analysis
Introduction
Notes: First is the car type, we have the following two possibilities, an Hyundai Tucson and a Toyota Celica.
We know from the app to expect different results.
Where do we try them?

## Slide 10: Car Type (ct’d)
SUV A.K.A Blue Sapphire
Sedan A.K.A Black Diamond
Windsor Road
Conclusion
Evaluation
Data Analysis
Introduction
Notes: First is the car type, we have the following two possibilities, an SUV and a Sedan.
We know from the app to expect different results.
We try them on Windsor road, low traffic volume and good conditions. Southeast Champaign, 1 mile approx. between philo and vine.

## Slide 11: Car Type (Results)
Chart: Station N°
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Sedan (i) | 2.78 | 2.85 | 2.63 | 2.39 | 2.25 | 2.45 | 2.71 | 2.13 | 2.4 | 2.46 | 2.65 | 2.8 | 2.48 | 2.53
Sedan (ii) | 3.01 | 3.08 | 2.49 | 2.49 | 2.31 | 2.62 | 2.53 | 2.15 | 2.31 | 2.39 | 2.56 | 2.76 | 2.57 | 2.57
SUV (ii) | 4.44 | 4.28 | 3.71 | 3.83 | 3.54 | 3.71 | 3.92 | 3.82 | 3.84 | 3.75 | 3.92 | 4.15 | 4.22 | 3.98
SUV (i) | 5.5 | 5.275 | 6.1 | 6.705 | 6.635 | 6.605 | 6.07 | 6.27 | 6.85 | 7.68 | 8.15 | 7.08 | 6.825 | 7.075
SUV (iii) | 4.57 | 4.08 | 4.06 | 4.58 | 4 | 4.7 | 4.2 | 4.25 | 4.44 | 4.44 | 4.76 | 4.61 | 4.76 | 4.93
Windsor Road Average | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36 | 2.36
Conclusion
Evaluation
Data Analysis
Introduction
Notes: We see that sedan has two very similar measurements, below in candid colors.
SUV with default settings is unreasonably high.
With changed settings it is still giving high results.
Since we are getting more consistent and reasonable results with SEDAN
(recall 63*IRI(si) = in/mi)

## Slide 12: Vehicle Speed
Choose Interstate Drive at north Champaign, full IRI data and low traffic. PCC.
Choose State St. Relatively low traffic and with IRI data all along. Asphalt surface and fair conditions.
Conclusion
Evaluation
Data Analysis
Introduction
Interstate Drive (PCI:80)
State Street (PCI: 40)
Notes: Choose two streets considering: Low traffic volumes which allow to try low speeds,

## Slide 13: Vehicle Speed
Conclusion
Evaluation
Data Analysis
Introduction
Chart: Interstate Drive (PCC)
| 1 | 2 | 3 | 4 | 5 | 6
CB (15mph) (i) | 2.2 | 2.24 | 2.04 | 2.1 | 1.98 | 2.44
CB (15mph) (ii) | 2.16 | 2.085 | 2.06 | 2.03 | 2.17 | 2.22
CB (30mph) (i) | 2.06 | 2.29 | 2.02 | 2.12 | 2.09 | 2.36
CB (30mph) (ii) | 2.435 | 2.485 | 2.22 | 2.1 | 2.215 | 2.235
Chart: State St. (AC)
| 1 | 2 | 3 | 4 | 5 | 6 | 7
CB (15mph) (i) | 3.085 | 2.815 | 2.8 | 3.225 | 3.34 | 3.08 | 3.12
CB (15mph) (ii) | 3 | 2.765 | 2.63 | 3.01 | 3.27 | 3.08 | 3.045
CB (30mph) (i) | 3.02 | 2.6 | 2.37 | 2.44 | 2.97 | 4.29 | 3.19
CB (30mph) (ii) | 2.83 | 2.71 | 2.61 | 2.4 | 2.86 | 4.21 | 3.13
Notes: Effect of speed is double: Greater accelerations possible, but also shorter wavelengths are registered when going at lower speeds.
Overall the results are similar
However there are relevant differences (10% ) in some stretches
State Street, ACC, shows a bump collected at 30mph not detected at 15mph
So here we can see a bit of the psychological part of the app: when driving at 15mph you don’t avoid any defects, when driving at 30mph you start avoiding things (improvement at the beginning) And lower wavelengths are not captured due to damping system.
Point defect in the road: At satange street theres a very noticeable sag, which produces a jump in IRI for a specific point, captured twice.

## Slide 14: 2) Accuracy
Conclusion
Evaluation
Data Analysis
Introduction
Chart: State Street (AC)
| 1 | 2 | 3 | 4 | 5 | 6 | 7
15 mph (i) | 3.085 | 2.815 | 2.8 | 3.225 | 3.34 | 3.08 | 3.12
15 mph (ii) | 3 | 2.765 | 2.63 | 3.01 | 3.27 | 3.08 | 3.045
30 mph (i) | 3.02 | 2.6 | 2.37 | 2.44 | 2.97 | 4.29 | 3.19
30 mph (ii) | 2.83 | 2.71 | 2.61 | 2.4 | 2.86 | 4.21 | 3.13
LIRI | 3.8352 | 2.5489 | 2.3161 | 4.6717 | 5.0268 | 4.2337 | 5.2478
RIRI | 3.6024 | 4.0838 | 4.3048 | 3.413 | 4.7191 | 4.648 | 4.723
Chart: Interstate Dr.(PCC)
| 1 | 2 | 3 | 4 | 5 | 6
15 mph (i) | 2.2 | 2.24 | 2.04 | 2.1 | 1.98 | 2.44
15 mph (ii) | 2.16 | 2.085 | 2.06 | 2.03 | 2.17 | 2.22
30 mph (i) | 2.06 | 2.29 | 2.02 | 2.12 | 2.09 | 2.36
30 mph (ii) | 2.435 | 2.485 | 2.22 | 2.1 | 2.215 | 2.235
LIRI | 2.8646 | 2.3911 | 2.5252 | 3.8826 | 3.488 | 2.6673
RIRI | 2.1622 | 1.6848 | 2.1109 | 1.8229 | 2.4187 | 2.3043
Notes: Now we compare with the actual measurements from Champaign City, using a profilometer. Easier in next graph

## Slide 15: Accuracy (ct'd)
Chart: Interstate Drive
| 1 | 2 | 3 | 4 | 5 | 6
CB (15mph) | 2.18 | 2.1625 | 2.05 | 2.065 | 2.075 | 2.33
CB (30mph) | 2.2475 | 2.3875 | 2.12 | 2.11 | 2.1525 | 2.2975
L.IRI | 2.8646 | 2.3911 | 2.5252 | 3.8826 | 3.488 | 2.6673
R.IRI | 2.1622 | 1.6848 | 2.1109 | 1.8229 | 2.4187 | 2.3043
Chart: State St.
| 1 | 2 | 3 | 4 | 5 | 6 | 7
CB (15mph) | 3.0425 | 2.79 | 2.715 | 3.1175 | 3.305 | 3.08 | 3.0825
CB (30mph) | 2.925 | 2.655 | 2.49 | 2.42 | 2.915 | 4.25 | 3.16
L. IRI | 3.8352 | 2.5489 | 2.3161 | 4.6717 | 5.0268 | 4.2337 | 5.2478
R. IRI | 3.6024 | 4.0838 | 4.3048 | 3.413 | 4.7191 | 4.648 | 4.723
Conclusion
Evaluation
Data Analysis
Introduction
Notes: Averaging our results we see that we are not specifically very on target, but when comparing to the already existing difference between the right and left measured IRI, the averaged results are within a tolerance level of acceptance. To show this go next:

## Slide 16: Relative Errors
Chart: State St.
CB (15mph) vs CMI | 0.67632 | 0.52636 | 0.59544 | 0.92487 | 1.5679 | 1.3609 | 1.9029
CB (30 mph) vs CMI | 0.79382 | 0.66136 | 0.82044 | 1.6224 | 1.9579 | 0.19089 | 1.8254
L.IRI vs R.IRI | -0.2328 | 1.5349 | 1.9886 | -1.2587 | -0.30776 | 0.4143 | -0.52478
Chart: Interstate Dr.
CB (15mph) vs CMI | 0.33341 | -0.12455 | 0.2681 | 0.78774 | 0.87836 | 0.15579
CB (30 mph) vs CMI | 0.26591 | -0.34955 | 0.1981 | 0.74274 | 0.80086 | 0.18829
L.IRI vs R.IRI | 0.70233 | 0.70628 | 0.4143 | 2.0597 | 1.0693 | 0.363
Conclusion
Evaluation
Data Analysis
Introduction
Notes: Averaging our results we see that we are not specifically very on target, but when comparing to the already existing difference between the right and left measured IRI, the averaged results are within a tolerance level.
How much more would it be reasonable to try to match these values?
Looking at the errors absolutely, there's a bigger “error” in State St., however in light it has bigger IRI values, we should consider that relative to the IRI value both have comparable errors.
Considering this, we explore some practical applications possible

## Slide 17: City of Champaign
Meeting with Champaign Public Works, we discussed:
  Scheduling
  Prioritization System
  Roughness Consideration
Conclusion
Evaluation
Data Analysis
Introduction
Notes: Scheduling:
  They record the condition………….each year
  Then report to Council…………..for contract award, cost and scope of work
  Aim to update information on a regular basis
Prioritizing:
  Based on: current condition, maintenance issues and citizen inputs
Roughness Consideration:
  High volume of the calls regarding maintenance requests......from citizens......for residential streets
  Mainly due to ride quality…..discuss about later

## Slide 18
City of Champaign
Conclusion
Evaluation
Data Analysis
Introduction
AAC: Asphalt over Asphalt Concrete
ABR: Asphalt over Brick
AC: Asphalt Concrete
APC: Asphalt over Portland Cement Concrete

## Slide 19
City of Champaign uses PCI (Pavement Condition Index) to evaluate pavement conditions:
Using IDEA (Interactive Data Exchange Application) to summarize the collected data
Conclusion
Evaluation
Data Analysis
Introduction
Champaign's Current Methodology
Notes: PCI:
Latest available data is from 2017

## Slide 20: Champaign's Current Methodology
Conclusion
Evaluation
Data Analysis
Introduction

## Slide 21: Practical Evaluation (Data Collection)
A section of the pavement network system rich in PCI data was selected:
  Delimited by Kirby Ave., Mattis Ave, John St. and Prospect Ave
  Having low traffic
  Presenting a good wide range of PCI
To contrast IRI results obtained via the app and current available PCI measurements
Conclusion
Evaluation
Data Analysis
Introduction

## Slide 22
PCI range in selected section:
  Max = 99 (Sangamon Dr.)
  Min= 14 (Daniel St.)
Conclusion
Evaluation
Data Analysis
Introduction
Practical Evaluation (Data Collection)

## Slide 23
To evaluate the capabilities of a model that predicts PCI through IRI data, we proposed:
  Linear Model
  K Nearest Neighbors Model
  Random Forest Model
Random Forest Model fits the best
In all cases a correct correlation was evidenced, but stronger correlation on very good or very bad values of PCI
Conclusion
Evaluation
Data Analysis
Introduction
Method | RMSE | R squared | Model Parameters
Linear Regression | 18.07 | 0.236 | a = 90.56, m = -10.44
Nearest Neighbor | 18.82 | 0.237 | K = 9
Random Forest | 13.77 | 0.575 | Mt=19
Practical Evaluation (Model Fitting)

## Slide 24
Conclusion
Evaluation
Data Analysis
Introduction
Practical Evaluation (Model Fitting)

## Slide 25
PCI is more detailed considering the actual distresses evidenced in the pavement.
Although distresses are captured to an extent by the app IRI measurement, they do not replace the PCI.
Specific issues may not be detected by a….
  Ex. Pot Holes if user avoids them
  In some cases, app failed to detect the road bumps
Extending the model with other data sources as well as a calibration by measuring some major roads could be the most economical and valuable methodology to enhance Champaign’s pavement management system.
Conclusion
Evaluation
Data Analysis
Introduction
Practical Evaluation (Results)

## Slide 26: Conclusions
Very disparate measurements between different vehicle categories (Sedan and SUV)
The final technical paper by WB is not out, we can’t qualify the model used
  The algorithm may have room for improvement
Operator dependency
  Keeping speed, vertical mounting, etc.
Tire pressure and other variables are not considered
  e.g. vehicle categorization is very broad
  Tire pressure may have an effect on the algorithm
Conclusion
Evaluation
Data Analysis
Introduction

## Slide 27: Conclusions (ct'd)
Will require a lot of work and calibrating before being widely used
Useful for local roads, track everything with same car, prioritize
Add an overhead camera, might help w/other Machine Learning
Having more accurate accelerometer data or better resolution could help
cityofnovi.org
Conclusion
Evaluation
Data Analysis
Introduction

## Slide 29
Special Mentions:
      Chris Sokolowski (CCPW)
      ERI
      Arturo (Aptech)
      RoadLabPro